## Slide 1: IENG 366
Managing Product & Production Planning
Reading: pp. 250 – 275.

## Slide 2: Product Planning

## Slide 3: New Product Development Stages
Conceptual
Technical Feasibility or Concept Definition
Development
Commercial Validation
Production
Product Support
Disposal Stage

## Slide 4: Figure 10-2 Formulation of a multispeciality project team designed to accomplish concurrent engineering in the stages of new product development. (From National Society of Professional Engineers, Engineering Stages of New Product Development, NSPE Publication #3018, Figure 22, p. 10.)

## Slide 5: Concurrent Engineering
A set of methods, techniques, and practices, that:
Increases consideration within design phase of factors from later in cycle
Creates a design of processes
Facilitates a reduction of the time required to translate design into products
Enhances the ability to meet user’s needs

## Slide 6: Special Considerations in Concurrent Design
Product Liability
Safety
Reliability
Maintainability
Availability
Ergonomics
Producibility

## Slide 7: Product Liability
Designer foresees unlikely conditions
Risks are reduced to the greatest extent possible
Product contains adequate warnings
Meets user’s reasonable expectations of safety

## Slide 8: Safety
Safeguards to Reduce or Eliminate Accidents Influenced By:
  Design
  Proven materials and components
  Proven manufacturing methods
  Clear instructions

## Slide 9: Reliability
  The probability that the product:
    Will perform a specified function
    Under specified conditions
    For a stated period of time

## Slide 10: Reliability

## Slide 11: Figure 10-4 Simple reliability models: (a) series; (b) simple parallel; (c) series in parallel; (d) parallel in series. S, switch; L, lamp; RT, total system reliability; dashed “boxes” indicate subsystems analyzed within [] in calculation.

## Slide 12: Figure 10-5 The bathtub curve.

## Slide 13: Reliability
Reliability is a measure of how often a system fails:
  How long (on average) you can run it until it stops working right
    How do you know that it’s not working right?
MTTF (Mean Time To Failure) or
  MTBF (Mean Time Between Failures)

## Slide 14: Maintainability
Maintainability is a measure of how long it takes to return a system to proper operation:
Sum of the times required to:
    diagnose the problem
    obtain repair parts / tools
    repair the failed components
    return the unit to operating conditions
MTTR (Mean Time To Repair)

## Slide 15: Availability
% Availability = MTTF
MTTF + MTTR
Availability is a function of Reliability and Maintainability:
  It is the percentage of time that you can count on using it for production

## Slide 16: Ergonomics
Human Factors Engineering
Science of designing machines, products, and systems to maximize the safety, comfort, and efficiency of the people who use them
One of primary goals is prevention of workplace injuries, illnesses, fatigue and accidents
May use simulations – replicas of workstations, aircraft, cars, trucks – and advanced sensors to collect data:
  Physiological Effort
  Cognitive Effort

## Slide 17: Table 10-2 Control Placement in Military Aircraft

## Slide 19: Production Planning
Activities involved in estimating and predicting how the product and the production system will be designed to meet the anticipated production quantities, quality, and profitability.

## Slide 20: Figure 11-3 Economic order quantity.

## Slide 21: Figure 11-4 Break-even chart.

## Slide 22: Figure 11-5 Break-even chart showing the effect of automation.
Δ BE
Incremental Automation Fixed Costs
Increased Automation Profits
Lowered Automation Variable Costs

## Slide 23: Figure 11-6 A more realistic break-even chart.

## Slide 24: Figure 11-7 A 90 percent learning curve.
=
=
If the first unit takes 1000 minutes to produce, then the second takes 900 minutes, and the fourth takes 810 minutes, … because the operator learns how to make it at a 90% rate of improvement.
Actual learning also has a forgetting effect when production stops (red lines), so the effect is averaged (black line).
Solving for
    =

## Slide 26: Layout Planning
Comprises all activities involved in selection for and transportation routes among departments, processes, work centers, machines, and service functions.

## Slide 27: Planning Manufacturing Facilities
Area Selection
  Location of markets
  Location of materials
  Transportation facilities
  Labor supply
  Location of other plants and warehouses
Community Selection
  Managerial preferences
  Community facilities
  Community attitudes
  Community, government and taxation
  Financial inducements
Site Selection
  Size of site
  Topography
  Utilities
  Waste Disposal
  Transportation facilities
  Land costs

## Slide 28: Common Errors in Facility Location Analysis
Labor cost miscalculations
Inadequate labor reservoir
Lack of distribution outlets
Underestimated importance of taxes
Purchasing unsuitable building

## Slide 29: Objectives of Layout Planning
Minimize materials-handling costs
Reduce congestion of personnel and material
Increase safety of personnel
Increase labor efficiency
Facilitate communication and coordination
Provide operations flexibility
Improve morale
Increase quality of working life

## Slide 30: Figure 11-2 Schematic representations of (a) product and (b) process layouts. (From Arthur C. Laufer, Production and Operations Management, 3rd ed., South-Western Publishing Company, Cincinnati, OH, 1984, pp. 232–233).

## Slide 31: Facilities Planning: Job Shop Layout
Drill
V. Mill
Lathe
L. Paint
Oven
H. Mill
P. Paint
Drill
Drill
Drill
Lathe
Lathe
Lathe
V. Mill
V. Mill
V. Mill
H. Mill
H. Mill
H. Mill
Grind
Grind
CMM
Receiving
Shipping

## Slide 32: Facilities Planning: Mass Production Layout
Drill
V. Mill
L. Paint
Oven
Drill
Lathe
H. Mill
Grind
CMM
Receiving
Shipping

## Slide 33: Facilities Planning: Group Technology Layout
Drill
V. Mill
L. Paint
Oven
Drill
Lathe
H. Mill
Grind
CMM
Receiving
Shipping
Drill
Grind

## Slide 34: Group Technology: Relationship (Incidence) Matrix
How to Identify Families – Incidence Matrix
Rows and Columns:
  Parts requiring operations on different machines
  Tools (in a CNC magazine) needed to produce part families
  Departments requiring technicians (shared head count)
  Departments requiring adjacent location
  Integrated Circuits requiring modularization
An entry in the incidence matrix means that there is a strong relationship between the row and column items

## Slide 35: Group Technology: Incidence Matrix
Rows represent Operations (index = i)
Columns represent Components (index = j)
Cell Entries are: (M i j )
  1 (or mark) - if the component requires the operation
  0 (or blank) - if the component does NOT require the operation
 | A-112 | A-115
Saw01 | 1 | 
Lathe01 |  | 
Lathe02 | 1 | 
Drill01 |  | 1
Mill02 |  | 1
Mill05 |  | 
Grind05 | 1 | 

## Slide 36: Group Technology: Solution Methods
Requirements:
Need for grouping similar items together, and identifying separable items
  Incidence Matrix: of related entities
    Tooling
    Equipment
    Parts
    Integrated Circuits
    Modular Components
  Solution Method: Matrix Triangularization
    King’s Algorithm* * method implemented for this class
    Direct Clustering Algorithm
    Kusiak’s Triangularization Method
    Ullman’s Design Structure Matrix

## Slide 37: Group Technology: Partitioning
 | A4 | A3 | A5 | A8 | A9 | A1 | A2 | A6 | A7 | A0
L01 | 1 |  |  |  |  |  |  |  |  | 
G05 |  |  |  |  |  | 1 |  |  |  | 
L02 |  | 1 | 1 | 1 | 1 | 1 |  |  |  | 
S01 | 1 | 1 | 1 | 1 | 1 | 1 |  |  |  | 
M02 |  |  |  |  |  |  | 1 |  |  | 
G06 |  |  |  |  |  |  |  |  |  | 1
D01 |  |  |  |  |  |  | 1 |  |  | 1
M05 |  |  |  |  |  |  |  | 1 | 1 | 1
Ideally, the cells form mutually exclusive blocks (as below). These blocks define the families:
  Family A consists of Components A1, A3, A4, A5, A8, and A9; which can be machined in a cell performing Operations G05, L01, L02, and S01
  Family B consists of Components A0, A2, A6, and A7; which can be machined in a cell performing Operations D01, G06, M02, and M05

## Slide 38: IENG 366 Engineering Management
Questions & Issues?