## Slide 1: IENG 366
Managing Production Operations
Reading: pp. 279 – 299.

## Slide 2: Production Operations
Major focus of production operations is on efficiency and effectiveness of processes
Production operations often include substantial measurement and analysis of internal processes

## Slide 3: Production Planning and Control Systems
Material Requirements Planning (MRP)
Manufacturing Resource Planning (MRP II)
Enterprise Resource Planning (ERP)
Synchronized Manufacturing (OPT)
Lean Manufacturing (TPS)

## Slide 4: Figure 11-8 Schedule of production lead times for product A.

## Slide 5: Figure 11-9 Examples of kanban cards. (From Hussein M. Reda, “A Review of ‘Kanban’—the Japanese ‘Just-in-Time’ Production System,” Engineering Management International, 4, 1987, p. 146).

## Slide 6: Figure 11-10 Mechanics of a simple kanban cycle. (1) Part produced at preceding station and P-kanban attached to it is sent to the store. (2) When the part is needed at a succeeding station, a W-kanban is sent to the store to withdraw the part. (3) At the store, the P-kanban is removed from the part and the W-kanban attached to it. The P-kanban is then collected in a “production-ordering” box. (4) At short time intervals, the P-kanban is then sent to the preceding station, constituting a production order. (5) The part with the W-kanban goes to the succeeding station to meet the demand. (6) The W-kanban is detached from the part and collected in a “withdrawal” box. (From Hussein M. Reda, “A Review of ‘Kanban’—the Japanese ‘Just-in-Time’ Production System,” Engineering Management International, 4, 1987, p. 146).

## Slide 7: Quality Engineering

## Slide 8: Malcolm Baldrige Quality Award Criteria
Leadership
Strategic Planning
Customer and market focus
Measurement, analysis, and knowledge management
Human resource focus
Process management
Business results

## Slide 9: International Organization for Standardization
ISO: developing highly specific standards since 1947
Generic Management Business Standards ISO 9000 – 1987
  Requires an organization to create processes in all functional areas that focus on customer needs and reasonable expectation and that validate requirements of quality
Primarily Environmental Management ISO 14000 – 1997

## Slide 10: Baldrige / ISO Difference
Baldrige criteria focuses on results and continuous improvement
ISO helps determine what is needed to maintain an efficient quality conformance system

## Slide 11: Basic Requirements of Quality Improvement
Management commitment
Focus on customer
  Internal or external
  Any person receiving the output
Continuous improvement of processes
Utilization of entire work force
Performance measures for the processes
Use of a rational, verifiable, improvement process:
  Define
  Measure
  Analyze
  Improve
  Control

## Slide 12: Quality: Understanding Process Variation
Three Aspects:
  Location
  Spread
  Shape
Variability is inherent in all processes.
SPC helps to:
  Quantify
  Communicate
  Make Decisions

## Slide 13: Quality Myth: Higher Quality  Higher Cost
$
Defect Rate
Quality Cost
Failure
Cost
Total Cost

## Slide 14: Very Often: Higher Quality  Lower Cost
Manufacturing Process
$20 / part
75% Conform
Textbook ex: Manufacture of Copier Part
Re-work Process
$4 / part
(15 good parts)
25% Non-conforming:
100 parts
(75 good parts)
(25 parts)
(10 scrap parts)

## Slide 15: Study finds excessive process variability responsible for high nonconformity rate
New SQC procedure implemented
  NOW: manufacturing non-conformities = 5%
  SAVINGS: $22.89 – $20.53 = $2.36 / good part
  PRODUCTIVITY: 9% improvement

## Slide 16: Quality Control Tools and Techniques
7 Tools of Ishikawa
  Histogram
  Pareto Chart
  Fishbone Chart (Cause & Effect Diagram)
  Check Sheet
  Defect Concentration Diagram
  Scatter (Plot) Diagram
  Statistical Process Control Charts
    Variables Charts
    Attributes Charts
    Individuals Charts
    Short Run SPC
Process Capability Measures
MIL STD 105D & Other Sampling Plans
Designed Experiments

## Slide 17: Ishikawa’s Tools: Histogram

## Slide 18: Ishikawa’s Tools: Pareto Chart
80% of any problem is the result of 20% of the potential causes
  Histogram categories are sorted by the magnitude of the bar
  A line graph is overlaid, and depicts the cumulative proportion of defects
  Quickly identifies where to focus efforts

## Slide 19: Ishikawa’s Tools: Cause & Effect Diagram
The purpose of the cause and effect diagram is to obtain as many potential influencers of a process, so that the problem solving can take a more directed approach.
Material
Machine
Man
Method
Environment
Skill Level
Low RPM
Orifice Clogs
Dusty
Humidity
Poor Conductor
Attention Level
Poor Mixing
Travel Limits
Temperature
Worn Parts
Poor Vendor
Bad Paint

## Slide 20: Ishikawa’s Tools: Defect Diagram
A defect concentration diagram graphically records the frequency of a defect with respect to product location.
  Obtain a digital photo or multi-view part print showing all product faces.
  Operator tallies the number and location of defects as they occur on the diagram.

## Slide 21: Ishikawa’s Tools: Check Sheet
Check sheets are used to collect data (values or pieces of information) in a consistent manner.
  List each of the known / possible problems
  Record each occurrence including time-orientation.
Title
Header Info: Date, Time, Location, Operator, etc.
List
of Prob
Types
Times of Problem Occurrence (periodic)
Statistics
For Prob Types
Time of Occurrence Statistics
Overall Statistics
Instructions, settings, comments, etc.
Raw Data recorded here

## Slide 22: Ishikawa’s Tools: Scatter Plot
A scatter plot shows the relationship between any two variables of interest:
  Plot one variable along the X-axis and the other along the Y-axis
  The presence of a relationship can be inferred or ruled out, but it cannot determine if a cause and effect relationship exists
Y
X
Y
X
Y
X

## Slide 23: Ishikawa’s Tools: SPC Charts
A control chart is like a sideways hypothesis test
  Detects a shift in the process
  Heads-off costly errors by detecting trends
0

2

2
0

2

2
2-Sided Hypothesis Test
Shewhart Control Chart
Sideways Hypothesis Test
CL
LCL
UCL
Sample Number

## Slide 24: Why Monitor Both Process Mean and Process Variability?
X-bar
R
X-bar
R
X-bar
R
Process Over Time
Control Charts
Ishikawa’s Tools: SPC Charts

## Slide 25: Use of Ishikawa’s Tools
Removing special causes of variation
Preparation for:
  hypothesis tests
  control charts
  process improvement
Reduce Variability
Identify Special Causes - Good (Incorporate)
Improving Process Capability and Performance
Characterize Stable Process Capability
Head Off Shifts in Location, Spread
Identify Special Causes - Bad (Remove)
Continually Improve the System
Statistical Quality Control and Improvement
Time
Center the Process
LSL 0 USL

## Slide 27: Figure 12-2 X-bar control chart.

## Slide 28: Figure 12-3 Four distributions of a quality characteristic in terms of the upper and lower specification limits (USL and LSL) and specification midpoint m.

## Slide 29: Control Charts (HW 03)
Variables
  Continuous measures
    L, W, H, Dia.
    Viscosity
    Temperature
Attributes
  Discrete measures
    Defectives
      (no value)
    Defects
      (diminished value)
Variables Charts
  X-bar charts
    Location of dist. Center
  R- (or s-charts)
    Range (spread) of dist.
Attributes Charts
  Variable / Fixed sample size
    Defectives
      p-, np-charts
    Defects
      u-, c-charts

## Slide 30: IENG 366 Engineering Management
Questions & Issues?