## Slide 1: The DMAIC Cycle
A Quick Review of the Components

## Slide 2: DMAIC Overview
DMAIC is a data-driven process for improving manufacturing, health care, service, and any business process. The acronym stands for the five steps of the process:
  Define
  Measure
  Analyze
  Improve
  Control
The cycle is repeated, quickly and continually improving the process and securing business advantages over the long term
It is the core process cycle for Six Sigma projects, and the steps may not be left out or performed out-of-order without eventual repercussion.

## Slide 3: Define
The first step of the process, the outcome of the DEFINE stage is to have a clear understanding of the problem to be addressed, the improvement level to be achieved (objective), and the relevant facts.
The DEFINE stage will clarify in-writing:
  A statement of the problem
    Including clarifying the relevant facts
  The process(es) targeted for improvement
    Including related/affected processes
  The user(s) affected by the problem
    Often referred to as the customer(s)
  The process outputs that are critical to quality
    CTQs have a direct impact on actual/perceived quality as defined by the user
  The scope of the project
    Defined boundaries that identify what is considered within/out-of bounds
These items result from a consensus of the project team members; and frequently, the project stakeholders

## Slide 4: measure
The second step of the process, MEASURE, is to decide on what are the inputs and output(s) of the process, and how to measure them. The need for good data is very important, and may take a lot of effort to create a system that:
  Defines the critical inputs in a test-ably measurable way
  Defines the process output(s) in a test-ably measurable way
  Defines a system for collecting the measurements (measurement plan)
  Tests the measurement system itself
  Collects sufficient data for testable results
Frequently, the measurement system is analyzed for adequacy (gauge R & R study) prior to data collection

## Slide 5: analyze
The third step (after collecting the data) is the ANALYZE stage. In this stage, one or more of the tools of SQC are used to identify the root cause(s) of poor process performance. During this stage, the team will:
  Identify sources of variation in the process output
  Identify relationship(s) between the process inputs and output(s)
  Identify (prioritize) the inputs that cause process variation
  Identify (quantitatively/qualitatively) the performance gap between the current process output and the output goal
One of the end results is that the analyze stage identifies a clear performance baseline from which to clearly identify significant and/or sustainable improvements

## Slide 6: improve
The IMPROVE stage is the fourth step in the cycle. In this stage, creative and quantitative tools are used to innovate the process, moving its measurable operation towards the goal. Solutions may be identified or improved by using tools like:
  Brainstorming
  5 Whys
  (Ishikawa) Fishbone Diagrams
  Design of Experiments
  Failure Mode & Effects Analysis (FMEA)
The outcome of this stage is to test-ably deploy improvements according to a detailed and documented implementation plan

## Slide 7: control
The last stage before the improvement cycle repeats is CONTROL. In this step, the team:
  Creates a plan to sustain the improvements
  Documents their efforts and the new baseline
  Implements a strategy to test-ably identify when the process is not operating as designed
    This may include the calculation of preliminary control limits, and recalculation of these limits if statistical process control charts are used
    Check sheets and variance reports are other tools that may be deployed to sustain improvements, provided that sufficiently detailed instructions are included to identify when assignable/special causes require action
This stage continues as long as monitored improvements result in continued success or until management decides to further improve the process (and the DMAIC cycle repeats)

## Slide 8: Sdsm&t six sigma green belt Req.s
For the SDSM&T Six Sigma Greenbelt Project, you will be required to document how each of these steps was performed during the implementation of an actual project. This includes documenting use of at least some of the tools appropriate to the project in some detail.
Due to the time-frame frequently inherent to the final stage, SDSM&T does not require completion of the CONTROL step, but it does require the documentation of the control plan, including identification of control chart types and calculation of preliminary control limits, if appropriate.
The Six Sigma Project may be done in conjunction with any of the following:
  Outside Employment (with permission of your employer)
  Co ops (with permission of your employer)
  Internships (with permission of your employer)
  Course Projects (with permission of your instructor)
  Senior Design projects … and others
The Six Sigma Project Report is required, and while you may use material from any of the above projects, the submitted document must be a stand alone report – see the Six Sigma Project Requirements document