## Slide 1: IENG 475 - Lecture 04
Lathe Operations

## Slide 2: Agenda
Introduction to Machining
  Processes
  Parameters
Turning
  Types of Cuts
  Lathe Terminology
  Process Parameters
Questions & Issues

## Slide 3: Fixture Quiz
What is the theoretical minimum number of points of contact necessary for:
  A vertically oriented rotational part?
  A prismatic part?
What is the vocabulary term for:
  A feature that “error-proofs” the use of a fixture?
  A component that constrains the primary and secondary planes for horizontally oriented rotational parts?
Explain two relative benefits for:
  Modular fixturing (vs. Permanent or General Purpose)

## Slide 4: Manufacturing Operations
Four classes of Processing Operations:
  Solidification Processes
  Particulate Processes
  Deformation Processes
  Material Removal Processes
Two classes of Assembly Operations:
  Mechanical Assembly
  Joining

## Slide 5: Machining
Variety of work materials can be machined
  Most frequently applied to metals
Variety of part shapes and special geometry features possible, such as:
  Screw threads
  Accurate round holes
  Very straight edges and flat surfaces
Good dimensional accuracy and surface finish
Wasteful of material
  Chips generated in machining are wasted material, at least in the unit operation
Time consuming
  A machining operation generally takes more time to shape a given part than alternative shaping processes, such as casting, powder metallurgy, or forming

## Slide 6: Machining Operations
Generally performed after other manufacturing processes (casting, forging, …)
  Other processes create the general shape of the workpart
  Machining provides the final shape, dimensions, finish, and special geometric details that other processes cannot create
Most important machining operations (by frequency) :
  Turning
  Drilling
  Milling
Other machining operations:
  Shaping and planing
  Broaching
  Sawing

## Slide 7: Primary Machining Parameters
Cutting Speed – (v)
  Primary motion
  Peripheral speed m/s ft/min
Feed – (f)
  Secondary motion
  Turning: mm/rev in/rev
  Milling: mm/tooth in/tooth
Depth of Cut – (d)
  Penetration of tool below original work surface
  Single parameter mm in
Resulting in Material Removal Rate – (MRR)
MRR* = v f d mm3/s in3/min
  where v = cutting speed; f = feed; d = depth of cut
  * general model, only!

## Slide 8: Turning Parameters Illustrated
Figure 22.5 ‑ Turning operation [Groover (2004), p.503]

## Slide 9: Drilling
Creates a round hole in a workpart
Contrasts with boring which can only enlarge an existing hole
Cutting tool called a drill or drill bit
Customarily performed on a drill press
Figure 21.3 (b) drilling
[Groover (2004), p.501]

## Slide 10: Milling Parameters Illustrated
Figure 21.3 ‑ Two forms of milling:
(a) peripheral milling, and (b) face milling
[Groover (2004), p.516]

## Slide 11: Machining Operations & Parameters
Operation Type | Speed | Feed | Depth of Cut
Turning: workpiece rotates single point cutting | Surface speed (periphery) of workpiece | Parallel to the workpiece axis* (*except parting/grooving) | Tool penetration below original work surface
Drilling: tool rotates single pass cutting | Surface speed (periphery) of tool | Parallel to the tool axis | Tool penetration below original work surface (depth of hole)
Milling: tool rotates multi-point cutting | Surface speed (periphery) of tool | Perpendicular to the tool axis | Tool penetration below original work surface

## Slide 12: Cut Types: Roughing & Finishing
Cut Type | Number of Passes | Speed | Feed | Depth of Cut
Roughing: removes large amounts to get close to shape | 1 + | Low | High 0.4 - 1.25 mm/ .015 - .050 in/ | High 2.5 - 20 mm .100 - .750 in
Finishing: achieves final dimensions, tolerances, and finish | 1 - 2 | High | Low 0.125 - 0.4 mm/ .005 - .015 in/ | Low 0.75 - 2.0 mm .030 - .075 in

## Slide 13: Turning
A single point cutting tool removes material from a rotating workpiece to generate a rotationally symmetric shape
Machine tool is called a lathe
Types of cuts:
  Facing
  Contour turning
  Chamfering
  Parting (Cut-off) / Grooving
  Threading

## Slide 14: Turning Parameters Illustrated
Figure 22.5 ‑ Turning operation [Groover (2004), p.503]

## Slide 15: Facing
Figure 22.6 (a) facing
Tool is fed
radially inward

## Slide 16: Contour Turning
Instead of feeding the tool parallel to the axis of rotation, tool follows a contour that is not necessarily straight (thus creating a contoured form).
Figure 22.6 (c) contour turning

## Slide 17: Right & Left Hand Tools
Right Hand Tool:
  Cuts from right to left
Left Hand Tool:
  Cuts from left to right

## Slide 18: Chamfering
Cutting edge cuts an angle on the corner of the cylinder, forming a "chamfer"
Figure 22.6 (e) chamfering

## Slide 19: Parting (Cutoff) / Grooving
Tool is fed radially into rotating work at some location to cut off end of part, or provide a groove
Figure 22.6 (f) cutoff

## Slide 20: Threading
Pointed form tool is fed linearly across surface of rotating workpart parallel to axis of rotation at a large feed rate, thus creating threads
Figure 22.6 (g) threading

## Slide 21: Engine Lathe
Figure 22.7
Diagram of an engine lathe, showing its principal components

## Slide 22: Chuck
Figure 22.8 (b) three‑jaw chuck

## Slide 23: Turret Lathe
Manual operation is replaced by a “turret” that holds multiple tools
  Tools are rapidly brought into action by indexing the turret
  Tool post is replaced by multi‑sided turret to index multiple tools
  Applications: high production work that requires a sequence of cuts on the part

## Slide 24: CNC Turret Lathe
Tool Turret
Spindle Speed
Spindle
Cross Slide
+ Z-axis
+ X-axis
Ways

## Slide 25: CNC Lathe: Air-Operated Chuck
Right Hand Profile Tool
Chuck

## Slide 26: CNC Lathe: Tool Turret
Tool Turret
Right Hand Profile Tool
Left Hand Profile Tool
Grooving / Parting Tool
Tool Holder

## Slide 27: Machining Calculations: Turning
Spindle Speed - N (rpm)
    v = cutting speed
    Do = outer diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per rev
Depth of Cut - d (mm/rev -or- in/rev)
    Do = outer diameter
    Df = final diameter
Machining Time - Tm (min)
    L = length of cut
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)
MRR =
π(Do2 – Df 2)f N
4

## Slide 28: Questions & Issues
Finish Fixturing & Start Machining This Week:
  Next Week: finish Machining (mill & drill), start Process Planning
    This means the Due Date for HW 00 must change to 06 FEB
    This also means that you must start HW 00 sometime soon …
  Following Week: NC / CNC Programming
Lab this week:
  Fixturing (manual tools & drill press)
Lab next week:
  Manual Lathe & Mill Operations:
    Rough & Finish Profiling Cuts
    Facing Cuts
    Parting Cuts
    Tool Changes
    Touch-Off