## Slide 1: IENG 475 - Lecture 05
Drilling & Milling Operations

## Slide 2: Agenda
Vertical Milling Equipment
Drilling Operations
Milling Operations
Machining Calculations
Questions & Issues

## Slide 3: Milling
Machining is an operation in which work is fed past a rotating tool with multiple cutting edges
  Axis of tool rotation is perpendicular to feed direction
  Usually creates a planar surface; other geometries possible either by cutter path or cutter shape
  Other considerations and terms:
    Milling is an interrupted cutting operation
    Cutting tool called a milling cutter, cutting edges called "teeth"
    Machine tool called a milling machine

## Slide 4: Vertical Mill
Figure 22.23 (b) vertical knee‑and‑column milling machine

## Slide 5: CNC Vertical Mill
Spindle Speed
Saddle
Table
Knee
Column
Head

## Slide 6: CNC Vertical Mill: Axes & Tools
Spindle
+ Z-axis
+ X-axis
– Y-axis
Tool Holder
Cutter
Alternate Tools (in quick-change magazine)
Air Vise

## Slide 7: Drilling
Creates a round hole in a workpart
Contrasts with boring which can only enlarge an existing hole
Cutting tool is called a drill or drill bit
Customarily performed on a drill press, but can be done on a vertical mill and on a lathe
Figure 21.3 (b) drilling

## Slide 8: Through Holes vs. Blind Holes
Figure 22.13 ‑ Two hole types: (a) through‑hole, and (b) blind hole
Through‑holes - drill exits the opposite side of work
Blind‑holes – drill does not exit work on opposite side

## Slide 9: Reaming
Used to slightly enlarge a hole, provide better tolerance on diameter, and improve surface finish
Figure 22.14 ‑ Machining operations related to drilling: (a) reaming

## Slide 10: Tapping
Used to provide internal screw threads on an existing hole
The tool is called a tap
Figure 22.14 (b) tapping

## Slide 11: Counterboring
Provides a stepped hole, in which a larger diameter follows a smaller diameter partially into the hole
Figure 22.14 (c) counterboring

## Slide 12: Accurate Hole-making
Sequence of Operations:
  Pilot (Center) Drill
  Drilling
  Boring
  Reaming

## Slide 13: Milling Parameters Illustrated
Figure 21.3 ‑ Two forms of milling: (a) peripheral milling, and (b) face milling

## Slide 14: Slab Milling
The basic form of peripheral milling in which the cutter width extends beyond the workpiece on both sides
Figure 22.18 (a) slab milling

## Slide 15: Slotting
Width of cutter is less than workpiece width, creating a slot in the work
  Figure 22.18 (b) slotting

## Slide 16: Conventional Face Milling
Cutter overhangs work on both sides
Figure 22.20
(a) conventional face milling

## Slide 17: End Milling
Cutter diameter is less than work width, so a slot is cut into part
Figure 22.20 ‑ (c) end milling

## Slide 18: Profile Milling
A form of end milling in which the outside periphery of a flat part is cut
Figure 22.20 (d) profile milling

## Slide 19: Pocket Milling
Another form of end milling used to mill shallow pockets into flat parts
Figure 22.20 (e) pocket milling

## Slide 20: Surface Contouring
Ball‑nose cutter is fed back and forth across the work along a curvilinear path at close intervals to create a three dimensional surface form
Figure 22.20 (f) surface contouring

## Slide 21: Machining Calculations: Drilling
Spindle Speed - N (rpm)
    v = cutting speed
    D = tool diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per rev
Machining Time - Tm (min)
  Through Hole :
    t = thickness
     = tip angle
  Blind Hole :
    d = depth
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)
MRR=
π D2 fr N
4

## Slide 22: Machining Calculations: Milling
Spindle Speed - N (rpm)
    v = cutting speed
    D = cutter diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per tooth
    nt = number of teeth
Machining Time - Tm (min)
  Slab Milling:
    L = length of cut
    d = depth of cut
  Face Milling:
    w = width of cut
    2nd form is multi-pass
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)
-or-
w d f
r
MRR
=

## Slide 23: Questions & Issues
Assignment(s):
  Complete HW 00 from Schedule Page
Lab this week & next:
  Manual Lathe & Mill Operations:
    Homing the machine(s)
    Tool Changes
    Touch-Off
    Facing Cuts
    Rough & Finish Profiling Cuts
    Parting Cuts*
    Pocketing Cuts*