## Slide 1: IENG 475 - Lecture 7
CNC Programming –
NC Coding & APT

## Slide 2: NC and CAD/CAM
Advantages of NC (vs. manual or fixed automation)
  Flexibility
    Easily reprogrammed (vs. fixed automation)
  Capability for complex work pieces
    Control more than two axes simultaneously (vs. manual)
    Programmed for sequences of operations
  Tool changing capability
    Single head accepting multiple tools from a magazine
  Reduced fixturing costs
    More axes, more tools fewer machine setups
  Repeatability (Quality)
    Reduced number of variability sources (vs. manual)

## Slide 3: NC Impact
Impact on Labor (vs. manual production)
  Skills change
    Manual capability Knowledge capability
  Increased wages
    Seniority tradition
      Not just a labor union tradition
    Increased operator responsibility
      Put the best people where the money is
  Increased productivity
    Fewer people needed to achieve output
    Lower cost for the product when produced in volume

## Slide 4: NC Axes of Motion
Conventions:
  Z-axis
    Brings tool in contact with the part
      – Z motion puts tool into part
      + Z motion takes tool out of part
  X-axis
    Direction of greatest travel
      + X follows right hand coordinate system rule
  Y-Axis
    Remaining primary axis
      + Y follows right hand coordinate system rule
  Remaining Axes
    Various degrees of freedom - ways to affect the part

## Slide 5: Positioning
Home
  Hard Home
  Soft (Part) Home
Incremental
  Current move endpoint is specified relative to the ending point for the last movement
Absolute
  Current move endpoint is specified relative to the home position
Position is the center point of the tool

## Slide 6: NC Code Formats
Words
  A word is a unitary piece of information
    Usually a parametric variable which takes on a value
  Examples:
    feed rate
    spindle speed
    x-coordinate
    coolant on/off condition
    interpolation mode condition

## Slide 7: NC Code Formats
Block Formats
  Fixed Sequential
    All word values specified in sequence (changed or not)
      Tedious, error-prone, inflexible, wasted space
  Block Address (Fixed Sequential with Tab Ignored)
    Specifies which words will be used within a block
      Tedious, error-prone, but more flexible, compact
  Tab Sequential
    Tab used instead of value in word sequence (no change)
      Tedious, but more flexible and less error-prone
  Word Address* (add Tab between words for ease in reading)
    Character specifies which word the value applies to
      least error-prone, more flexible and compact

## Slide 8: G Code
N words
  Block numbers
G words
  Preparatory commands (motion control)
F words, S words, T words
  Feed, speed, tool control
X words (Y words, Z words, …)
  Position control
M words
  Miscellaneous (machine control)

## Slide 9: Milling Touch-Off: Our Lab Convention
Touch-Off Point (Soft/Part Home)
X=0, Y=0, Z=0
top, front, left corner of the stock
X
Y
Z

## Slide 10
0
0
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Write an NC program to cut the letter P 1” deep and centered in the grid at a feed of 5.5 IPM and a spindle speed of 1800 RPM using a tool that is numbered 04.
Assume the soft home position is as defined in our lab, and that the hard home position is at x = 0, y = 0, z = 10.
Assume that we want it in absolute coordinates.
x ( i )
( j )
y

## Slide 11
0
0
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Write an NC program to cut the letter P 1” deep and centered in the grid at a feed of 5.5 IPM and a spindle speed of 1800 RPM using a tool that is numbered 04.
Assume the soft home position is as defined in our lab, and that the hard home position is at x = 0, y = 0, z = 10.
Assume that we want it in incremental coordinates.
x ( i )
( j )
y

## Slide 12: Questions & Issues
Assignment(s):
  Start HW 01 from Schedule Page
Lab (current):
  Lathe & Mill Operations:
    Homing the machine(s) (Hard Home)
    Tool Changes
    Touch-Off (Soft Home)
    Facing & Grooving Cuts
    Rough & Finish Profiling Cuts*
    Parting Cuts*
    Pocketing Cuts*
  NC Lathe Programming – See Schedule Page link

## Slide 13: HELP: HW 01 NC Calculations
Coordinates
for point of tangency
(Use with HW 01)

## Slide 14: APT
Automatically Programmed Tool
  NC language instead of an NC code
    Abbreviated English format
    Symbolic addresses
  Describes motion of the tool edge(s) relative to the surfaces of the part
    Drive surface
    Part surface
    Check surface
  Computer computes center point of the tool for the user
    This creates a CL (cutter location) data file that is converted to G Code by a post-processor

## Slide 15: APT
Four types of APT statements:
  Geometry statements
    Define the geometric elements that define the part
  Motion statements
    Describe the path taken by the cutting tool
  Post-processor statements
    Apply to the specific machine tool, such as feeds, speeds, feature actuation (coolant on, etc)
  Auxiliary statements
    Miscellaneous statements that identify the part, tool, tolerances, etc.

## Slide 16: APT TO, ON, PAST Modifiers
P4
L2
L3
P3 C1
P1
L1
P2
0
1
2
3
4
5
6
7
8
GOFWD/ L3, TO, L2
GOFWD/ L3, ON, L2
GOFWD/ L3, PAST, L2
GOFWD/ L3, TO, P2
GOFWD/ L3, ON, P2
GOFWD/ L3, PAST, P2

## Slide 17: APT Example

## Slide 18
L0
L10
L1
L2
L3
L4
L5
L6
L7
L8
L11
L12
L13
L14
L15
L16
L17
L18
Write an APT program to cut the letter P centered in the grid at a feed of 5.5 IPM and a spindle speed of 1800 RPM using a tool that is ½” in diameter.
Assume the soft home position is as defined in our lab, and that the hard home position is at P0, and plane PL1 is the correct depth.
P10 (10" above)
C1
C2

## Slide 19
0
0
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
Write an APT program to cut the outside of the letter P centered in the grid at a feed of 5.5 IPM and a spindle speed of 1800 RPM using a tool that is ½” in diameter.
Assume the soft home position is as defined in our lab, and that the hard home position is at P0, and plane PL1 is the correct depth for the cut (1” below surface).
P10 (10" above)
C1
L12
L8
L4
P2
P1
P5
P4
P3
L0
0, 0, -1
8, 0, -1
P0 (10" above)
2, 0, 10

## Slide 20: Computers & NC
NC
  Numerical Control
    Electric control based on paper tape, hard wired CPU
DNC
  Direct Numerical Control
    Single, fast mainframe computer
    Central control of each NC machine (time sharing)
    Each NC machine cabled to central CPU
CNC
  Computer Numerical Control
    Each CNC has its own CPU, maybe retrofitted
    Production continues if central CPU goes down

## Slide 21: Computers & NC
DNC / HNC
  Distributed / (Hierarchical) Numerical Control
    Library of programs centrally maintained
    Distributed production data acquisition and central database
    Centralized production control adapting to changing conditions
    Limited loss of production if central CPU is down
CAD/CAM
  Computer-Aided Design / Computer-Aided Mfg
    Stronger design / manufacturing database
    Enhanced knowledge (CPU), off-line error-checking
      More productive, flexible; less tedious and error-prone

## Slide 22: Questions & Issues
Assignment(s):
  Start HW 02 from Schedule Page
Lab (current):
  Lathe & Mill Operations:
    Homing the machine(s) (Hard Home)
    Tool Changes
    Touch-Off (Soft Home)
    Facing & Grooving Cuts
    Rough & Finish Profiling Cuts*
    Parting Cuts*
    Pocketing Cuts*
  NC Lathe Programming – See Schedule Page link