## Slide 1: IENG 475 - Lecture 08
Group Technology –
Parts Classification & Coding (PC & C)

## Slide 2: Assignment
HW Assignment
  Download GT PC&C notes & HW 03 from the Schedule page
    Use the copies of the Opitz & Vuosa-Praha GT codes to classify and code the part on HW 3
  Turn in HW 03 at the start of the 21 FEB class!
LAB Assignment
  Download NC Lathe Programming Lab from the Schedule page
    HINT: Cut a 90o arc (unless you want to do a lot of geometry or SolidWorks CAD work)
    Circular interpolation is backward on a lathe …
  Test (simulate) your code on the tablets in lab before running your part on the lathe – next week!

## Slide 3: Group Technology (GT)
Philosophy:
  Use the similarity of current products to simplify the design and manufacturing of new products
Some Applications:
  Identify and reuse similar process plans
  Identify and reuse similar CNC programs
  Identify the equipment that may be best used in a particular machine cell
  Identify and eliminate redundant inventory
Requirement:
  A taxonomy of part characteristics

## Slide 4: Benefits of GT
Facilitates formation of part families and machine cells
Quick retrieval of designs, drawings, & process plans
Reduces design duplication
Provides reliable workpiece statistics
Facilitates accurate estimation of machine tool requirements and logical machine loadings
Permits rationalization of tooling setups, reduces setup time, and reduces production throughput time
Allows rationalization and improvement in tool design
Aids production planning and scheduling procedures
Improves cost estimation and facilitates cost accounting procedures
Provides for better machine tool utilization and better use of tools, fixtures, & people
Facilitates NC part programming.
        (Ham)

## Slide 5: How to Identify Groups
Similar Design Attributes
  Size of parts
  Geometric shape of parts
  Materials
  Technique: Parts Classification & Coding
Similar Manufacturing Attributes
  Common processing steps (routings)
  Common tools and fixtures
  Technique: Production Flow Analysis
Similarity groupings are called Part Families

## Slide 6: Parts Classification & Coding
Group Technology applied to parts is called Parts Classification & Coding (PC&C)
Methods:
  (Human) Visual Inspection
    Least sophisticated
    Least accurate (repeatable)
    Least expensive
  (Computer) Feature Recognition
    Most expensive to develop
    Most accurate (repeatable)

## Slide 7: Typical PC&C Attributes
Part Design Attributes:
  Basic external shape
  Basic internal shape
  Major dimensions
  Length/diameter ratio
  Minor dimensions
  Material type
  Tolerances
  Surface finish
  Part function
      (Groover)
Part Mfg Attributes:
  Major process
  Minor operations
  Major dimension
  Length/diameter ratio
  Operation sequence
  Surface finish
  Machine tool
  Production time
  Batch size
  Annual production
  Required Fixtures
  Cutting tools

## Slide 8: PC&C Code Types
Three PC&C Code Types:
  Hierarchical (monocode)
    Succeeding position code values depend on the preceding code values
      Very detailed & compact, but complex
      Tend to exaggerate minor differences
  Chain (polycode)
    Individual code values do not depend on the other code positions
      Robust (least affected by minor differences)
      Least compact for same level of detail (30+ digits)
  Hybrid
    Mixture of hierarchical and chain types

## Slide 9: GT PC&C Code Examples
Vuosa-Praha
  4 digits (monocode)
Opitz
  Basic - 5 digits (monocode)
  Enhanced - 9 digits (hybrid)
DCLASS
  8 digits (monocode)
MICLASS
  12 digits (polycode)
KK-3
  21 digits (hybrid)

## Slide 10: GT PC&C Vuosa-Praha Code Ex.
Construct the specified GT codes for the following part, initially made from
a nodular
graphitic (grey iron) casting
. Support your answer on each digit for credit. Note:
Below
the axis is an interior section view,
above
is the un
-
sectioned exterior view.
Milled
Locating
Groove
Axis
Through Hole
Pilot
Æ
10.50 mm
Ø
7
5
± .0254
mm
1
87
.
5
0 mm
R
adius
0.0254 mm on Spur Gear
Roots and Crests
M 12 In
terior
Thread
Along Axis
Rotational, geared, through hole in axis
→ 5
→ 4
→ 5
→ 7
(Rotational) diameter (75) w/in 40 – 80, L/D ratio (2.5) is w/in 1 – 4
Material is grey iron
(Rotational) thread in axis (1) and groove (3) → combination 1 + 3

## Slide 11: GT PC&C Opitz Code Example
Construct the specified GT codes for the following part, initially made from
a nodular
graphitic (grey iron) casting
. Support your answer on each digit for credit. Note:
Below
the axis is an interior section view,
above
is the un
-
sectioned exterior view.
Milled
Locating
Groove
Axis
Through Hole
Pilot
Æ
10.50 mm
Ø
7
5
± .0254
mm
1
87
.
5
0 mm
R
adius
0.0254 mm on Spur Gear
Roots and Crests
M 12 In
terior
Thread
Along Axis
Rotational, L/D ratio is w/ in 0.5 – 3
→ 1
→ 6
→ 2
→ 3
→ 6
(rotational) Ext. shape is stepped to both ends, w/ functional groove
Plane surface machining has external groove
(rotational) Int. shape (hole) is smooth w/ thread
(rotational) Gear teeth form a spur gear

## Slide 12: PC&C Opitz Supplemental Code
Construct the specified GT codes for the following part, initially made from
a nodular
graphitic (grey iron) casting
. Support your answer on each digit for credit. Note:
Below
the axis is an interior section view,
above
is the un
-
sectioned exterior view.
Milled
Locating
Groove
Axis
Through Hole
Pilot
Æ
10.50 mm
Ø
7
5
± .0254
mm
1
87
.
5
0 mm
R
adius
0.0254 mm on Spur Gear
Roots and Crests
M 12 In
terior
Thread
Along Axis
Diameter is greater than 50 mm and less than/equal to 100 mm
→ 2
→ 1
→ 7
→ 6
Material is nodular graphitic cast iron
Diameter(s) have 2 and 4 decimals of accuracy specified
Initial form is a cast component

## Slide 13: CAPP
Computer-Aided Process Planning
  Requires a pre-existing GT coding
Two Methods:
  Variant
    Retrieve a process plan for a similar part
    Modify the process plan, adapting it to the new part
      New part process plan is a variation on the family STANDARD process plan
  Generative
    Based on the new part’s attributes, develop (generate) a new process plan
      Generally requires a feature recognition system to identify a compatible part family, then an expert system to step through the family processing options

## Slide 14: Why CAPP?
Benefits of CAPP:
  Reduces skill required of planner
  Reduces process planning time
  Reduces process planning & manufacturing costs
  Creates more consistent plans
  Produces more accurate plans
  Increases productivity!

## Slide 15: Where does this GT improved productivity impact the Manufacturing Cost Breakdown
Fig. 2.5 Breakdown of costs for a manufactured product [Black, J T. (1991)]
Selling Price
15%
5%
Eng’g
Manufacturing Cost
R & D
Profit
Admin, Sales, Mktg, etc.
15%
25%
40%
Mfg Cost
50%
26%
Parts & Mat’ls
Direct Labor
Plant / Mach. Depreciation, Energy
Indirect Labor
12%
12%