## Slide 1: IENG 475 - Lecture 09
Sensors, Actuators, and Relay Control Logic

## Slide 2: Assignment
Reading & Assignment
  Obtain ISO Fluid Logic Notes handout from Materials Page before next class

## Slide 3: Definitions
Sensor: a device that allows the measurement of some physical quantity of interest.
Transducer: a device that converts one physical quantity into another (more useful) physical quantity.
Analyzer: a device that compares two or more quantities to provide information for decision making.
We tend to refer to all of these as sensors.

## Slide 4: Classes & Types of Sensors
Four major classes of sensors:
  Tactile (contact - limit switches)
  Proximity & Range (non-contact)
  Vision (recognition, orientation)
  Miscellaneous (temp, pressure, strain)
Two types of sensors:
  Analog (continuous physical quantity)
  Digital (discrete physical quantity)

## Slide 5: Examples
Position
  Limit switches
    ac/dc current
    location
  Potentiometers
    dc voltage
    angular / linear
  Resolvers
    ac voltage phase shift
    angular
  Encoders
    ac/dc current
    angular / linear location
    Incremental / Absolute
Velocity
  Tachometer
    Analog
      dc voltage
      angular velocity
    Digital
      pulse frequency
      angular / linear velocity
Temperature
    Capacitive
    Resistive
    Thermistors
Pressure
    Piezo-electric
    Resistive

## Slide 6: Examples
Transducers
  ADCs -
    Analog to Digital Converters
  DACs -
    Digital to Analog Converters
  Frequency to Voltage Converters
  Voltage to Frequency Converters
Analyzers
  Counters
  Timers
  Computers
  Ultra-Sonics
  Radar
    distance
    frequency shift
  Vision Systems

## Slide 7: Considerations
Noise Immunity: the ability to discriminate the desired quantity from the background signals.
  Validity: the surrogate quantity’s ability to represent the desired, physical quantity.
  Shielding: preventing false responses from entering the measurement system.

## Slide 8: Considerations
Noise Immunity (continued):
  Hysteresis: the quantity of signal required to trigger an increase in measured value is greater than that required to trigger a decrease in measured value.
Voltage
0 1 2 3 4 5
On
Off
On Threshold
Off Threshold
Hysteresis

## Slide 9: Considerations
Response Time: the time between when a measurable change occurs and when the change in quantity is detected.
Calibration: establishing the relationship between the measured physical variable (input) and the quantified response signal (output).

## Slide 10: Measures
Resolution: the smallest change in the quantity that can be detected.
    Mill Example: How close can I position the center of the tool to a point in the work envelope?
Repeatability: the ability to consistently obtain the same quantification.
    Mill Example: Can I consistently return to a previously visited point?
Accuracy: the ability to obtain the true, desired quantification.
    Mill Example: If I tell it to go to a point in the work envelope, will it go where I told it to?

## Slide 11: Actuators
Linear Action: Stroke Length
  Cylinders:
    Hydraulic
      High force (1000 psi, typical)
      Low to medium speed
      Leaks, noise, bulk, cost
    Pneumatic
      Medium force (100 psi, typical)
      High speed
      Noise; intermediate mess, bulk & cost
  Solenoids (Electromagnetic):
      Low force (< 10 lbf, typical)
      Medium speed
      Quiet, clean, small, cheap
  Linear Slides (Electro-mechanical):
      Medium Force (50 – 400 lbf, typical)
      Low to medium speed
      Quiet, clean, medium size & cost

## Slide 12: Rotary Actuators (Drives)
Rotary Action (may be converted to linear):
  Motors
    Hydraulic (rotary vanes)
      High power
      Low to medium speed, medium precision
      Leaks, noise, bulk, cost
    Pneumatic (rotary vanes)
      Medium power
      High speed, low precision
      Noise; intermediate mess, bulk & cost
    Electric
      Low power
      Medium speed, high precision
      Quiet, clean, small, cheap

## Slide 13: Electric Motors
Stepper Motors
  DC pulses result in fixed angular motion
  Pairs of coils activated
  Lower speed (to avoid ringing)
  Lower power & holding torque

## Slide 14: Electric Motors
Diff. Amp.
Servo Motors
  Require feedback to operate (tachometer)
  AC
    speed controlled by the frequency of the power supplied to the motor
    more powerful
  DC
    speed controlled by the magnitude of the voltage supplied to the motor
    holding torque
Velocity In
Feedback
Tachometer
Motor
Shaft
+
–

## Slide 15: Control Loops
Open Loop:
  Distance from position to endpoint is used to compute axis motions, control signals are sent to axis drives, and at the end of the motion time, it is assumed that the desired position has been reached.
Closed Loop:
  Distance from position to endpoint is used to compute axis motions, control signals are sent to axis drives, and the error between the desired and the attained position is fed back to the control system until the error tolerance has been reached.

## Slide 16: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
  Mechanical Stops:
    Range of motion is limited by stops
    “Reprogrammed” by changing the position of the stops
    Examples: Pneumatic “bang-bang robots”
Cam
Follower
Piston
Cylinder
Stops

## Slide 17: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
Cam
Follower

## Slide 18: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
Cam
Follower

## Slide 19: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
Cam
Follower

## Slide 20: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
Cam
Follower

## Slide 21: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
  Mechanical Stops:
    Range of motion is limited by stops
    “Reprogrammed” by changing the position of the stops
    Examples: Pneumatic “bang-bang robots”
Cam
Follower
Piston
Cylinder
Stops

## Slide 22: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
  Mechanical Stops:
    Range of motion is limited by stops
    “Reprogrammed” by changing the position of the stops
    Examples: Pneumatic “bang-bang robots”
Cam
Follower
Cylinder
Piston
Stops

## Slide 23: Motion Control
Hard Automation
  Mechanical Cams:
    Shape of the cam determines motion of the follower
    “Reprogrammed” by changing out the cams
    Examples: Automatic screw machines, gun stocks
  Mechanical Stops:
    Range of motion is limited by stops
    “Reprogrammed” by changing the position of the stops
    Examples: Pneumatic “bang-bang robots”
Cam
Follower
Cylinder
Piston
Stops

## Slide 24: Motion Control
Point to Point
  Starting and ending points are given, but the path between them is not controlled
  Advantage: simple, inexpensive controller
  Example: Peck drilling

## Slide 25: Motion Control
Continuous Path
  Both endpoints and the path between them are controlled
  Advantage: complex shape capability
  Example: NC contouring

## Slide 26: Interpolation
Linear:
  1. Find the axis motion times: divide each axis displacement by the max drive rate for that axis.
  2. Find the max motion time of all the axis motion times.
  3. For each axis, divide the axis motion time by the max motion time to find the operating % for that axis motor.
a
b
X
Y
x(t)
y(t)

## Slide 27: Interpolation
Circular:
  Approximated by linear interpolation chords.
  Approximation determined by one out of three tolerances: Inner Tolerance, Outer Tolerance, or Total Tolerance.
a
b
X
Y
x(t)
y(t)
c
r

## Slide 28: Interpolation
Inner Tolerance:
  Chords are located inside the arc

## Slide 29: Interpolation
Outer Tolerance:
  Chords are located outside the arc

## Slide 30: Interpolation
Total Tolerance:
  Inner and Outer tolerances are equal