## Slide 1: IENG 475 - Lecture 12
Ladder Logic
Programming of PLCs

## Slide 2: Review: PLC System Diagrammed
Power Supply
CPU
Memory
Input
Block
Output
Block
Programming
Unit

## Slide 3: PLC Memory Map
Input Block
Output Block
Output Image Table
Input Image Table
User Program (Rungs)
Internal Processor Work Area(s)

## Slide 4: PLC Scan Time
Time to complete one processing cycle
  Typically on the order of milliseconds
  Depends on length of program
Scan Time Diagrammed:
Update Output Image Table
Update Input Image Table
Logic (rung) Evaluation
I/O Scan
Program Scan
Scan Time
Repeat Cycle

## Slide 5: Counters
Siemens: CTU, CTUD, CTD
  Counter types are count up, count up/down, count down
    Counter addresses are C000 – C255
    Range is -32767 to +32767 transitions
  Count changed only when rung input condition goes from false to true
  PV is the preset value:
    the value to count up to for CTU, CTUD, and
    the value to count down from (CTD) before output changes
  Can cascade counters to obtain longer counts

## Slide 6: Counters
CTU: up counters
  Increments when CU rung goes from false to true
  Output stays OFF until count = PV
  R is the input signal to reset the count
CTD: down counters
  Decrements when CD rung goes from false to true
  Output stays OFF until count = 0
  LD is the input signal to reset the count
CTUD: up/down counters
  Increments when CU rung goes from false to true
  Decrements when CD rung goes from false to true
  Output turns on when count ≥ PV
  R is the input signal to reset the count
CU
CD
R
PV
C33
+100
CTUD
DECR
INCR
RST
CD
LD
PV
C33
CTD
DECR
+100
LD
CU
R
PV
C33
CTU
INCR
+100
RST

## Slide 7: Using Counters: Penguin Migration
System Definition:
  N.O. through-beam photosensor input (PNGN HR) detects penguins as they waddle up the ramp to a truck to be driven to a safe location
  Truck will hold 33 000 penguins
  An output (CLS DR) closes the ramp door when the truck is full
PNGN HR
CU
R
PV
C33
CTU
+32 000
RSTRT
CU
R
PV
C34
CTU
+1 000
C33
C34
PNGN HR
CLS DR
RSTRT

## Slide 8: Timer Outputs
Siemens: TON, TONR, TOF
  Timer addresses are:
    T0, T32, T64, T96: 1ms time base
    T1-T4, T33 –T36, T65-T68, T97-T100: 10ms time base
    T5-T31, T37-63, T69-T95, T101-T255: 100ms time base
  Time incremented only while rung input condition is true
  Timer is reset when input rung goes false for TON; true for TOF; or when R input goes true for TONR
  Can cascade timers to obtain longer delays

## Slide 9: Timers
TONR: retentive timer on-delay
  Starts timing when rung becomes true
  Output stays OFF until retained time delay is over
  R resets the timer when R rung is true
TOF: timer off-delay
  Starts timing when rung goes false
  Output stays ON until time delay is over
  Timing starts over at zero if rung becomes true
TON: timer on-delay
  Starts timing when rung becomes true
  Output stays OFF until time delay is over
  Timing starts over at zero if rung becomes false
IN
PT
T33
+100
TONR
10ms
STRT
IN
PT
T33
+100
TOF
10ms
STRT
IN
PT
T37
+10
TON
100ms
STRT
T33
RST
R

## Slide 10: Using Timers: Penguin Truck Garage
System Definition:
  N.O. through-beam photosensor input (TRCK HR) detects a truck driven into a garage
  Truck driver needs 1 minute of garage light (GRG LGHT) to exit garage
  An output (SHRK DR) opens the shark trap 10 s later to keep penguins on truck
TRCK HR
T36
T37
TRCK HR
SHRK DR
IN
PT
T36
+ 600
TOF
100ms
IN
PT
T37
+1 000
TON
10ms
GRG LGHT
T36

## Slide 11: Sequencers
Allen-Bradley: SQO
  Sequencer addresses are 901 - 932
    Width of a step is 8 bits
    Limited to 100 steps at a maximum
  Sequence can be event driven (similar to counter) or time driven (similar to timer)
  When AC = PR, advance to next step and set AC to 0000
    PR is the event count / dwell time
    Event Driven:
      Step AC is incremented at the false to true transition of rung input condition
    Timer Driven*:
      Step AC is incremented at 0.1 s intervals only when rung input condition is true
  RST rung resets the sequencer to step 0
SEQ
RST
901
(AB)
100ms
* Our Focus:

## Slide 12: Sequence (Drum) Matrix
Bit Address Outputs
Step
0
1
2
3
4
5
...
Count/Dwell
1.0
5.1
2.0
30.0
0.1
5.0
...
A
1
1
1
0
0
0
...
B
0
1
0
0
0
0
...
C
0
0
1
1
0
0
...
F
0
1
1
0
0
1
...
E
0
0
0
0
0
1
...
G
0
0
0
0
0
1
...
H
0
1
1
0
0
1
...
D
0
1
1
0
0
1
...

## Slide 13: Using Sequencers: Penguin Wash
System Definition:
  N.O. N2OH4 sensor input (PNGN SMLL) detects a smelly penguin in the washer
  Penguin gets a 1 minute cold water spray with the drain opened, door closed
  Drain closes and Penguin tank gets filled with water and soap (2.5 minutes)
  Penguin gets a 4 minute soap & warm water wash, drain closed and spinner on
  Penguin gets a 3 minute warm water rinse as wash water drains (no agitation)
  Tank waits for 1 minute to fill w/ water & Penguin Softener, spinner on, drain closed
  Tank drains for 1.5 minutes with spin on
  Penguin is fluffed by hot air while spinning for 2 minutes
  Door opens and beeper signals that the clean penguin is available (for 10 seconds)
  Door stays open and system resets
Outputs:
  A: Door Lock (1-closed, 0-open)
  B: Water Valve (1-opened, 0-closed)
  C: Soap Valve (1-opened, 0-closed)
  D: Drain Valve (1-opened, 0-closed)
  E: Spinner Motor (1-on, 0-off) F: Penguin Softener Valve (1-on, 0-off)
  G: Hot Air Blower (1-on, 0-off) H: Beeper (1-on, 0-off)

## Slide 14: Using Sequencers: Penguin Wash
Bit Address Outputs
Step
0
1
2
3
4
5
6
7
Count/Dwell
600
1500
2400
1800
600
900
1200
100
A
1
1
1
1
1
1
1
0
B
1
1
1
1
1
0
0
0
C
0
0
1
0
0
0
0
0
F
0
0
0
0
1
0
0
0
E
0
0
1
0
1
1
1
0
G
0
0
0
0
0
0
1
0
H
0
0
0
0
0
0
0
1
D
0
1
0
1
0
1
0
0

## Slide 15: Using Sequencers: Penguin Wash
Ladder Logic Network:
PNGN SMLL
SEQ
RST
901
(AB)
100ms
RESET

## Slide 16: Good Control System Design
Clearly define signals, assigning good mnemonics and complete descriptions
Set up truth table(s)
Intelligently minimize logic gates and signals required
Professionally diagram the control system(s)
Carefully complete the system documentation
  ID and cross-reference signals, sources, sinks

## Slide 17: Logic Simplification
Why simplify:
  Price of “real estate” (gates take space, cost of space)
  Less complex is easier to maintain (fewer gates)
  Avoid errors (in logic)
Why NOT to simplify:
  Price of “real estate” (FPGA / ROM chips take little space)
  Less complex is easier to maintain (obfuscated logic)
  Avoid errors (in minimizing logic)
Might be best to design both ways, and carefully evaluate the trade-offs

## Slide 18: Simplification Methods
Boolean Logic
  See link on Materials page (put in notebook)
Karnaugh Maps
  Depends on “logical adjacency”
    Output = B • A + B • A
    Output = B • (A + A)
    Output = B • 1
    Output = B
  Depends on pattern recognition ability
  Usually best when ≤ 4 variables (although 5 or 6 variables, and MEV methods could be employed)

## Slide 19: Karnaugh Maps
Summarized: Most efficiently cover all the map’s “1’s”
  Enter the “1’s” (and “Don’t Cares”) into K-map for EACH output
  Circle the largest group of adjacent “1’s”
    Shade the “1’s” covered by the group
    Continue until all the “1’s” in the map have been covered (circled & shaded)
  “Don’t Cares” (X’s or Ø’s) are covered and included ONLY if they make a grouping larger (simpler) by a power of 2
    Be careful that what is specified as a “Don’t Care” REALLY doesn’t matter
  Evaluate the groupings to determine which variable(s) aren’t needed
    both the variable & it’s complement (opposite) appear in grouping
  Express as the Sum Of Products from each grouping (minterm)

## Slide 20: Questions & Issues