## Slide 1: IENG 475 - Lecture 13
Introduction to Robotics

## Slide 2: Three Laws for Robots
Asimov’s Three Laws:
  A robot must not harm a human being, nor through inaction allow one to come to harm.
  A robot must always obey human beings, unless that is in conflict with the first law.
  A robot must protect itself from harm, unless that is in conflict with the first two laws.
Applications (Four D’s of Robotics):
  Dirty
  Dull
  Difficult
  Dangerous

## Slide 3: Robotics Technology I
Definition of a Robot (RIA):
  A robot is a reprogrammable, multi-functional manipulator designed to move material, parts, tools, or specialized devices through programmed motions for the performance of a variety of tasks.
Key Aspects:
  Reprogrammability
  Multiple functions
  FLEXIBILITY

## Slide 4: Degrees of Freedom
A Degree Of Freedom (DOF) is another means to affect a workpiece - one more way to accomplish a task.
Each joint on a robot is a DOF:
  Rotational joints
  Prismatic (linear) joints
Robot DOF:
  Number of different joints from base through wrist
    Does NOT include the end-effector (gripper, tool)
    Purchase price of a robot does not include an end-effector

## Slide 5: Degrees of Freedom
Wrist DOF (similar to an airplane):
  Roll: axial rotational motion
  Pitch: radial rotational motion (up/down)
  Yaw: radial rotational motion (left/right)
    Many robots do not have yaw - it can be faked if the joints align properly with the workpiece!

## Slide 6: End-Effectors
Two kinds of end of arm manipulators:
  Grippers (hold an object)
    Vacuum cups
    Hooks, forks
    Inflatable
    RCC
      Remote Center Compliance
  Tools (perform work on an object)
    Spray applicators
    Welding tools
    Lasers, water jets
    Extruders
Electromagnetic
Adhesive
Scoops, ladles
Fingered grippers
Drills, routers
Grinders
Screw drivers, riveters
Test equipment

## Slide 7: Drives and Motion Controls
Typical Drives (sound familiar?)
  Hydraulic
  Pneumatic
  Electric
Typical Motion Control (sound familiar?)
  Hard Automation (mechanical cams)
  Axis Limit (bang-bang / mechanical stops)
  Point-to-Point (Pick and Place)
  Contouring (Continuous Path)
    Linear Interpolation
    Circular Interpolation

## Slide 8: Work Envelope
The work envelope is the set of all points that the end-effector can reach.
The selection of a robot depends on many things, but configuration and envelope are important first cut criteria:
  Positions that must be reached must fall within the work envelope
  Obstacles that must be avoided are addressed by the configuration
    ex: cylindrical robots cannot reach around an obstacle, but they are best suited for tending many casting / molding / milling machines

## Slide 9: Five Industrial Robot Configurations
Cartesian
  Gantry crane is an inverted Cartesian configuration
Cylindrical
Polar
Articulated / Anthropomorphic / Revolute
SCARA
  Selective Compliance Assembly Robot Arm
  Primary rotary joints have vertical axes
  Important for Pick and Place (ie: electronic assembly applications)

## Slide 10: Work Envelope - Cartesian

## Slide 11: Cartesian
Three linear axes (x, y, z)
  Base travel, Reach, Height
Advantages:
  Easy to visualize
  Rigid structure
  Easy to program off-line
Disadvantages:
  Can only reach in front of itself
  Requires large floor space for envelope size
  Axes are hard to seal against debris

## Slide 12: Work Envelope - Cylindrical

## Slide 13: Cylindrical
One rotational, two linear axes (, r, z)
  Base rotation, Reach, Height
Advantages:
  Can reach all around itself
  Reach and height axes rigid
  Rotational axis easy to seal against debris
Disadvantages:
  Cannot reach above itself
  Rotation axis is less rigid, linear axes hard to seal
  Can’t reach around obstacles
  Horizontal motion is circular

## Slide 14: Spherical (Polar)
One linear, two rotational axes (, r, )
  Base rotation, Reach, Elevation angle
Advantages:
  Long horizontal reach
  Can usually reach above itself
Disadvantages:
  Can’t reach around obstacles
  Generally has short vertical reach
  Horizontal and vertical motion is circular

## Slide 15: Anthropomorphic/Articulated Envelope

## Slide 16: Anthropomorphic / Articulated
Three (or more) rotational axes (, , )
  Base rotation, Elevation angle, Reach angle
Advantages:
  Can reach above or below obstacles
  Largest envelope for least floor space
Disadvantages:
  Difficult to program off-line
  Two or more ways to reach a point
  Most complex configuration (construction)
  Horizontal motion is circular

## Slide 17: Work Envelope - SCARA

## Slide 18: SCARA
Two rotational, one linear axes (, , z)
  Base rotation, Reach angle, Height
Advantages:
  Height axis is rigid
  Large envelope for floor space
  Can reach around horizontal obstacles
Disadvantages:
  Two ways to reach a position
  Difficult to program off-line
  Highly complex arm
  Horizontal motion is circular

## Slide 19: Robot Components
Robot Arm
End-effector
Controller
Power Supply
Programming Device
  On-line Devices:
    Teach Pendant
    Lead-through / Walk-through
    Dumb Terminal
  Off-line Devices:
    Computer (PC)

## Slide 20: Ex. Anthropomorphic Spec Sheet

## Slide 21: Performance Specifications
Payload
  Maximum Payload is the maximum mass that the arm can move at reduced speed at the rated precision
  Nominal Payload is the maximum mass that the arm can move at maximum speed at the rated precision
  Effective Payload is the mass that may be moved after the mass of the end-effector has been subtracted
    Ratings are highly dependant on the size and shape of the payload

## Slide 22: Performance Specifications
Speed
  Maximum speed is that of the tip of the arm at full extension with all joints moving simultaneously
  The maximum speed must NOT be used to estimate cycle times
    Use the “standard” 12 in. pick and place cycle time for rough estimates
    Use a physical simulation for critical estimates
    May require motion to a lower inertia posture
Repeatability
Resolution
Accuracy

## Slide 23: Performance Specifications
“Standard” 12 in. Pick and Place Cycle
  The time to execute the following motion sequence (seconds):
    Move down one inch
    Grasp rated payload
    Move up one inch
    Move across twelve inches
    Move down one inch
    Release the payload
    Move up one inch
    Return to starting location

## Slide 24: Positioning
Envelope Coordinates
  World Frame
    Usually expressed in terms of workcell’s coordinate axes
    Often include cartesian coordinates
Tool Center Coordinates
  Tool Frame
    Usually expressed in terms of tool’s coordinate axes
    May include world cartesian coordinates
Joint Coordinates
  Robot Frame
    (Encoder) values of the joint positions at each programmed point

## Slide 25: Example Spec Sheet

## Slide 26: Example Articulated Spec Sheet

## Slide 27: Example SCARA Spec Sheet