## Slide 1: IENG 475 - Lecture 15
Robot Programming in ACL

## Slide 2: Assignment
Last Lab (this period)
  Write program to do the 12” Pick and Place Cycle in ACL commands for a total of 5 cycles. (Assume a new payload magically appears each time)
Remaining Laboratory Periods
  Teach positions and run Robot Program
  Complete NC Programming
    Estimate times, plan for production

## Slide 3: Programming
Teach Pendant
Lead-through / Walk-through / Dummy Robot
Languages:
  AML, AML/2
  ARMBASIC
  Karel
  RAIL
  RAPL
  SCORBASE
  VAL, VAL II
  Wave ...

## Slide 4: Programming
Documentation:
  Position Diagram(s)
  Position Table
  I/O Signal Table(s)
  Program Listing
    Well Commented
  Operating Instructions / Safety Procedures
  Program Metrics
    Cycle Times
    Program Size
  Bill of Materials (Parts List)
  Wiring Diagram(s)

## Slide 5: Robot Programming
Good Programming Practices:
  Always start a program with motion(s) from the HOME position
  Always signal the start of automated operations by triggering a warning output
  Always have an interrupt signal for critical error conditions
  Always design programs to be “fail-safe” - to fail in a safe condition
  Generously comment your programs

## Slide 6: Anthropomorphic Spec Sheet

## Slide 7: ACL Programming – ER V+ Robot
Advanced Command Language
  Similar to BASIC
  Programmed at keyboard in EDIT mode
  Positions can be taught with teach pendant, or with keyboard in DIRECT mode
Programming Sequence:
  Teach positions
  Sketch positions
  Program
    Motions & Logic & I/O
  Verify (slow speed) & Edit as necessary
  Save program

## Slide 8: Program Editing Commands
Edit starts a new program
  EDIT program_name
S goes to the start of the program / line
  S line_n
L lists the lines of a program
  L n1 n2
Del erases the current line of a program
* precedes a comment line
Exit quits the editor and validates
Copy copies a program to program2
  COPY program1 program2
Rename changes the name to program2
  RENAME program1 program2
Remove deletes a program from RAM

## Slide 9: Operation Commands
Run executes a saved program
  Run program1
A aborts program & motions
  A - or - Ctrl+A from keyboard
Stop aborts running program(s)
  STOP program1
  STOP
Suspend halts program execution
  SUSPEND program1
Continue continues program execution
  CONTINUE program1

## Slide 10: Motion Commands
Home sends the robot to known position
  Use this as the start and end of every program
Open opens the gripper
Close closes the gripper
Speed sets the speed for the axes of motion
  SPEED value(1..100)
Move moves robot in point to point
  MOVE position
MoveL moves robot in linear motion
  MOVEL position
MoveC moves robot in circular motion
  MOVEC position1 position2
NOTE: adding a D at the end of a move command allows the robot to delay the next axis motion until all movement is complete
  Ex. MoveD position, MoveLD position, MoveCD position

## Slide 11: Location Commands
Here Stores the position as joint coordinates
  HERE position1
HereR Stores the position as relative to last in joint coords
  HERER position2 position1
Teach Stores the position as cartesian coordinates
  TEACH position
TeachR Stores the position as relative to last in cartesian
  TEACHR position2 position1
SetP Transfers positions as variables
  SET P position1 = position2
SetPV Changes a joint coordinate value
  SETPV position axis value
SetPVC Changes a cartesian coordinate value
  SETPVC position coord value

## Slide 12: Program Control Loop Commands
If checks condition of two variables
  IF variable1 condition variable2
AndIf combines If conditions
  ANDIF variable1 condition variable2
OrIf combines If conditions
  ORIF variable1 condition variable2
Else subroutine for false If condition
  ELSE
EndIf ends an If routine
  ENDIF
For looping command
  FOR variable1 = variable 2 TO variable3
EndFor end of looping command
  ENDFOR

## Slide 13: Program / Branching Commands
Label sets a label for branching to
  LABEL number(0..9999)
Goto sends program to a branch
  GOTO label_n
Gosub transfers control to another program, suspending current until subprogram is completed
  GOSUB program2

## Slide 14: Programming Variables Commands
Global creates global variables
(all programs can use any global variables)
  GLOBAL variable1 … variable2
Define creates local variables
(only current program can use local variables)
  DEFINE variable1 … variable2
DimG dimensions an array of size n global variables
  DIMG variable[n]
Dim dimensions an array of size n local vars
  DIMG variable[n]
Set assigns value to variable1
  SET variable1= variable2 operation variable3
  Operations can be + - * / SIN COS TAN ATAN EXP LOG MOD OR AND

## Slide 15: Programming Variables Commands
Print Displays text on screen
  PRINT “string”
PrintLn Starts a new line & displays text on screen
  PRINTLN “string”
Read Displays a prompt string & gets input
  READ “prompt” variable
Get Waits for one keyboard character press
  GET variable

## Slide 16: Robotics Lab
Inking Mask on Pad
Inking Mask & Pad
Base & Pallets
Initial Position
Final Position
Fixture Pins

## Slide 17: Questions & Issues
Finish producing your lid corners & monikers this week.
Finish your chess piece program verifications
  Verify on CNC Lathe
    Watch for tool interference
    Watch for chuck interference
    Detail handling of workpiece origin & running program(s)
Finalize design & select production methods
  Consolidate programs in Team Folders
  Organization for production – personnel, tools
  Schedule time for last week’s demo
  – by the end of this week
No lab next week – Monday will be last exam
In-class review & class assessment this Wednesday