## Slide 1: IENG 475 - Lecture 16
Logic Minimization

## Slide 2: Good Control System Design
Clearly define signals, assigning good mnemonics and complete descriptions
Set up truth table(s)
Intelligently minimize logic gates and signals required
Professionally diagram the control system(s)
Carefully complete the system documentation
  ID and cross-reference signals, sources, sinks

## Slide 3: Logic Simplification
Why simplify:
  Price of “real estate” (gates take space, cost of space)
  Less complex is easier to maintain (fewer gates)
  Avoid errors (in logic)
Why NOT to simplify:
  Price of “real estate” (FPGA / ROM chips take little space)
  Less complex is easier to maintain (obfuscated logic)
  Avoid errors (in minimizing logic)
Might be best to design both ways, and carefully evaluate the trade-offs

## Slide 4: Simplification Methods
Boolean Logic
  See link on Materials page (put in notebook)
Karnaugh Maps
  Depends on “logical adjacency”
    Output = B • A + B • A
    Output = B • (A + A)
    Output = B • 1
    Output = B
  Depends on pattern recognition ability
  Usually best when ≤ 4 variables (although 5 or 6 variables, and MEV methods could be employed)

## Slide 5: Review: PLC Memory Map
Input Block
Output Block
Output Image Table
Input Image Table
User Program (Rungs)
Internal Processor Work Area(s)

## Slide 6: Review: PLC Scan Time
Time to complete one processing cycle
  Typically on the order of milliseconds
  Depends on length of program
Scan Time Diagrammed:
Update Output Image Table
Update Input Image Table
Logic (rung) Evaluation
I/O Scan
Program Scan
Scan Time
Repeat Cycle

## Slide 7: Karnaugh Map Example #1
Steps:
  Set up Truth Table to cover all possible state of I/O
    Left side is Inputs and Current Output states
    Right side is Next Output state
      Show a “1” only when you want to turn the Output “on”

## Slide 8: Karnaugh Map Example #1
Steps:
  Convert the Truth Table to Karnaugh Map
    Labels are the pattern of Inputs/Current Output states (Grey Scale)
    Cell entries are the “1”s of the Next Output State

## Slide 9: Karnaugh Map Example #1
Steps:
  Interpret the Karnaugh Map
    Group the “1s” into the largest power of 2 adjacent members: (1, 2, 4, 8, 16 …)
    Read the groups:
      Connection within group members is “AND” (●)
      Connection between groups is “OR” (+)
      Equation is written as Sum of Products
A
B
+
B shows up in both 0 and 1, within group, so it drops out
A shows up in both 0 and 1, within group, so it drops out

## Slide 10: Karnaugh Map Example #2
Steps:
  Set up Truth Table to cover all possible state of I/O
    Left side is Inputs and Current Output states
    Right side is Next Output state
      Show a “1” only when you want to turn the Output “on”

## Slide 11: Karnaugh Map Example #2
Steps:
  Convert the Truth Table to Karnaugh Map
    Labels are the pattern of Inputs/Current Output states (Grey Scale)
    Cell entries are the “1”s of the Next Output State

## Slide 12: Karnaugh Map Example #2
Steps:
  Interpret the Karnaugh Map
    Group the “1s” into the largest power of 2 adjacent members: (1, 2, 4, 8, 16 …)
    Read the groups:
      Connection within group members is “AND” (●)
      Connection between groups is “OR” (+)
      Equation is written as Sum of Products
A & C show up only as 1s in the group, but B shows up in both 0 and 1, within group, so it drops out
A shows up as only as a 1 & B shows up only as a 1 in group, but C shows up in both 0 and 1, within group, so it drops out
+
A●C
A●B

## Slide 13: Karnaugh Map Example #3
A shows up in both 0 and 1, within group, so it drops out, leaving B and C both showing up only as 1s (so they stay in)
A and C both show up only as 1s in the group so they stay, but B shows up in both 0 and 1 within group, so it drops out
These ends of the K-map are also adjacent (they only change by one bit position), so they can be grouped.
B●C
A●C
+

## Slide 14: Karnaugh Map Example #4
A & D both show up only as 1s in the group (they stay), but B & C show up in both 0 and 1, within group, so they drop out
C & D both show up only as 1s in the group so they stay, but A & B show up as both 0 and 1 within group, so they drop out
It is OK for groups to overlap in order to get larger groupings in powers of 2
A●D
C●D
+

## Slide 15: Karnaugh Map Example #5
A & D both show up only as 1s in the group (they stay), but B & C show up in both 0 and 1, within group, so they drop out
B & C & D all show up only as 1s in the group so they stay, but A shows up as both 0 and 1 within group, so it drops out
It is OK for groups to overlap in order to get larger groupings in powers of 2
A●D
B●C● D
+

## Slide 16: Karnaugh Map Example #6
A & B both show up only as 1s (so they stay), but both C & D show up as both 0 and 1, within group, so they drop out
B & C both show up only as 1s in the group so they stay, but A & D both show up in both 0 and 1 within group, so they drop out
These four ends of the K-map are also adjacent (they only change by one bit position), so they can be grouped.
A●B
B●C
+

## Slide 17: Karnaugh Map Example #7
A & D both show up only as 1s in the group (they stay), but B & C show up in both 0 and 1, within group, so they drop out
B & C & D all show up only as 1s in the group so they stay, but A shows up as both 0 and 1 within group, so it drops out
It is OK for groups to overlap in order to get larger groupings in powers of 2
A●D
B●C● D
+
The Ф is a symbol for “Don’t Care”. They can be included if it makes a group larger by a power of 2, but do not have to be covered

## Slide 18: Karnaugh Maps
Summarized: Most efficiently cover all the map’s “1’s”
  Enter the “1’s” (and “Don’t Cares”) into K-map for EACH output
  Circle the largest group of adjacent “1’s”
    Shade the “1’s” covered by the group
    Continue until all the “1’s” in the map have been covered (circled & shaded)
  “Don’t Cares” (X’s or Ø’s) are covered and included ONLY if they make a grouping larger (simpler) by a power of 2
    Be careful that what is specified as a “Don’t Care” REALLY doesn’t matter
  Evaluate the groupings to determine which variable(s) aren’t needed
    both the variable & it’s compliment (opposite) appear in grouping
  Express as the Sum Of Products from each grouping (minterm)

## Slide 19: System Documentation Example: Penguin Migration & Truck Garage
System Definition – Migration Ramp:
  N.O. through-beam photosensor input (PNGN HR) detects penguins as they waddle up the ramp to a truck to be driven to a safe location
  Truck will hold 33 000 penguins
  An output (CLS DR) closes the ramp door when the truck is full
System Definition – Truck Garage:
  N.O. through-beam photosensor input (TRCK HR) detects a truck driven into a garage
  Truck driver needs 1 minute of garage light (GRG LGHT) to exit garage
  An output (SHRK DR) opens the shark trap 10 s later to keep penguins on truck

## Slide 20: System Documentation Example: Penguin Wash Sequencer
System Definition:
  N.O. N2OH4 sensor input (PNGN SMLL) detects a smelly penguin in the washer
  Penguin gets a 1 minute cold water spray with the drain opened, door closed
  Drain closes and Penguin tank gets filled with water and soap (2.5 minutes)
  Penguin gets a 4 minute soap & warm water wash, drain closed and spinner on
  Penguin gets a 3 minute warm water rinse as wash water drains (no agitation)
  Tank waits for 1 minute to fill w/ water & Penguin Softener, spinner on, drain closed
  Tank drains for 1.5 minutes with spin on
  Penguin is fluffed by hot air while spinning for 2 minutes
  Door opens and beeper signals that the clean penguin is available (for 10 seconds)
  Door stays open and system resets
Outputs:
  A: Door Lock (1-closed, 0-open)
  B: Water Valve (1-opened, 0-closed)
  C: Soap Valve (1-opened, 0-closed)
  D: Drain Valve (1-opened, 0-closed)
  E: Spinner Motor (1-on, 0-off) F: Penguin Softener Valve (1-on, 0-off)
  G: Hot Air Blower (1-on, 0-off) H: Beeper (1-on, 0-off)

## Slide 21: System Documentation Example: Penguin Wash Sequencer Output Table
Bit Address Outputs
Step
0
1
2
3
4
5
6
7
Count/Dwell
600
1500
2400
1800
600
900
1200
100
A
1
1
1
1
1
1
1
0
B
1
1
1
1
1
0
0
0
C
0
0
1
0
0
0
0
0
F
0
0
0
0
1
0
0
0
E
0
0
1
0
1
1
1
0
G
0
0
0
0
0
0
1
0
H
0
0
0
0
0
0
0
1
D
0
1
0
1
0
1
0
0

## Slide 22: System Documentation Example: Circuit Diagram (PLC Rungs, Pt. 1)
PNGN HR
CU
R
PV
C33
CTU
+32 000
RSTRT
CU
R
PV
C34
CTU
+1 000
C33
C34
PNGN HR
CLS DR
RSTRT

## Slide 23: System Documentation Example: Circuit Diagram (PLC Rungs, Pt. 2)
TRCK HR
T36
T37
TRCK HR
SHRK DR
IN
PT
T36
+ 600
TOF
100ms
IN
PT
T37
+1 000
TON
10ms
GRG LGHT
T36
PNGN SMLL
SEQ
RST
901
(AB)
100ms
RESET

## Slide 24: Questions & Issues