# Hand Out 02:  NC Programming Notes

The following NC codes are commonly found in CNC programs for machining:

## G Words

G00	Rapid traverse

G01	Linear interpolation

G02	Circular interpolation, CW

G03	Circular interpolation, CCW

G04	Dwell (non-modal)

G05	Hold until operator restarts

G06	Parabolic interpolation

G07	unassigned EIA - reserved

G08	Acceleration (non-modal)

G09	Deceleration (non-modal)

G10-12	unassigned EIA

G13-16	Axis selection

G17	X-Y Plane

G18	X-Z Plane

G19	Y-Z Plane

G20-24	unassigned EIA

G25-29	unassigned – available for individual use

G30-32	unassigned EIA

G33	Thread cutting, constant lead

G34	Thread cutting, increasing lead

G35	Thread cutting, decreasing lead

G36-39 	unassigned – available for individual use

G40	Cutter compensation, cancel

G41	Cutter compensation, left

G42	Cutter compensation, right

G43	Cutter compensation, inside corner

G44	Cutter compensation, outside corner

G45-49	unassigned EIA

G50	Reserved for adaptive control (non-modal)

G51	Cutter compensation, +/0 (non-modal)

G52	Cutter compensation, –/0 (non-modal)

G53	Linear shift, cancel

G54	Linear shift, X

G55 	Linear shift, Y

G56 	Linear shift, Z

G57 	Linear shift, XY

G58 	Linear shift, XZ

G59 	Linear shift, YZ

G60-69 	unassigned EIA

G70	Inch format

G71	Metric format

G72	Circular interpolation, CW (3-D)

G73	Circular interpolation, CCW (3-D)

G74	Multi-quadrant circle interpolation, off

G75	Multi-quadrant circle interpolation, on

G76-79 	unassigned EIA

G80	Fixed-cycle, off

G81-89	Fixed cycles (manufacturer dependent)

G90	Absolute positioning

G91	Incremental positioning

G92	Set origin of coordinate system (non-modal)

G93	Inverse time feed rate (V/D)

G94	Inches (mm) per minute feed rate

G95	Inches (mm) per revolution feed rate

G96	Constant surface speed feet (m) per minute

G97	Revolutions per minute

G98-99 	unassigned EIA

## Circular interpolation occurs within a plane, and is specified by a block containing the following (in order):

- Plane code (G word)

- Direction code (G word)

- 1st destination coordinate (X or Y word)

- 2nd destination coordinate (Y or Z word)

- 1st incremental coordinate for arc center, from initial tool position (I or J word)

- 2nd incremental coordinate for arc center, from initial tool position (J or K word)

- Feed word (if necessary)

## X, Y, Z (A, B, C) Words

# These words provide coordinates for the axes of motion.  A, B, and C specify rotation about the X, Y, and Z axes, respectively.

### I, J, K Words

These specify the coordinates for the arc/circle center, always incrementally from the initial tool position (for circular interpolation).

# F Words

Specify the feed rate or thread lead.

### S Words

Specify the spindle speed.

# R* Words

These are words used to specify the radius of an arc/circle (for circular interpolation) (*highly machine dependent).

### T Words

Specify the tool number (turret position) to use.  If more than two digits, are used, the second two digits are the offset number.

### M Words

M00	Program stop (non-modal) (command starts after current block)

M01	Optional stop (non-modal) (command starts after current block)

M02	End of program (non-modal) (command starts after current block)

M03	Start spindle, CW

M04	Start spindle, CCW

M05	Stop spindle (command starts after current block)

M06 	Change tool

M07	Coolant 1 on

M08	Coolant 2 on

M09	Coolant off (command starts after current block)

M10	Clamp

M11	Unclamp

M12	Synchronization code (command starts after current block)

M13	Start spindle, CW and coolant on

M14	Start spindle, CCW and coolant on

M15	Motion in positive direction (non-modal)

M16	Motion in negative direction (non-modal)

# M17-18	unassigned EIA

M19	Oriented spindle stop

M20-29 	unassigned EIA – available for individual use

M30	End of tape/data, rewind (command starts after current block)

M31	Interlock bypass

M32-35 	unassigned EIA

M36-39 	unassigned EIA – available for individual use

M40-46	unassigned EIA – machine dependent

M47	Return to program start (non-modal)

M48	Cancel M49

M49	Feed/speed bypass override

M50-57 	unassigned EIA

M58	Cancel M59

M59	Bypass constant surface speed updating

M60-89 	unassigned EIA

M90-99	Reserved for user

The usual steps in generating NC code files are:

- A part model is created using a CAD system.

- The CAD part model is transferred to a CAM system (unless integrated with the CAD program).

- The geometry of the work piece stock is specified.

- The paths, tools, feeds, speeds, and depth of cuts for each machining pass are specified.

- The CAM software generates a CL (cutter location) data file (often APT-like).

- A post-processor reads the CL data file, and generates the NC code specific to the machine tool controller.

The NC code is transferred (often by RS-232 link) to the machine tool controller, where the operator initiates production of the part on the machine tool.  With the spread of more capable CAD/CAM packages, it has become uncommon for the engineer to do much manual NC programming.  However, editing NC code is a common task.

Example NC Problem

The following workpiece is to have a finishing pass around its periphery (see Figure 1).  The pertinent machining data is:  (a) cutter diameter is 0.25 inches; (b) feed rate is 6 inches per minute; (c) cutting speed is 300 surface feet per minute; (d) the tool home position is at (2, 2, 8); and (e) the part home position is at (4, 4, 0), referencing the lower, left corner of the top of the workpiece.  (Adapted from Chang, T. C., Wysk, R. A., & Wang, H. P.  (1991).  Computer-Aided Manufacturing.  Englewood Cliffs, NJ:  Prentice-Hall.  pp. 253-255.)

P2			                  P3	                   P7				          P8

P4		      P6

P5

(4, 4, 0)

Y

P1

Z		X

P0

(2, 2, 8)

Figure 1.  Workpiece for NC machining.

#### Geometry Calculations

P1:	x = 4 – ½ (0.25) = 3.8750

y = 4 – ½ (0.25) tan 67.5o = 3.6982

P2:	x = P1x = 3.8750

y = 4 + 5 + ½ (0.25) = 9.1250

P3:	x = 4 + 2.5 – 1 + ½ (0.25) = 5.6250

y = P2y = 9.1250

P4:	x = P3x = 5.6250

y = 9.125 – ½ (0.25) = 9.0000

P5:	x = 4 + 2.5 = 6.5000			i = 4 + 2.5 – P4x = 0.8750		offset to circle center

y = 9.125 – 1 + ½ (0.25) = 8.1250		j = 4 + 5 – P4y = 0.0000		offset to circle center

P6:	x = 4 + 2.5 + 1 – ½ (0.25) = 7.3750 	i = 4 + 2.5 – P5x = 0.0000		offset to circle center

y = P4y = 9.0000 				j = 4 + 5 – P5y = 0.8750		offset to circle center

P7:	x = P6x = 7.3750

y = P3y = 9.1250

P8:	x = 4 + 5 + ½ (0.25) tan 67.5o = 9.3018

y = P7y = 9.1250

Table of Cutter Locations

|  | Absolute Coordinates | Incremental Coordinates* |
| --- | --- | --- |
| Position | X | Y | Z | I | J | K |
| P0 | 2.0000 | 2.0000 | 8.0000 |  |  |  |
| P1 | 3.8750 | 3.6982 | 0.0000 |  |  |  |
| P2 | 3.8750 | 9.1250 | 0.0000 |  |  |  |
| P3 | 5.6250 | 9.1250 | 0.0000 |  |  |  |
| P4 | 5.6250 | 9.0000 | 0.0000 |  |  |  |
| P5 | 6.5000 | 8.1250 | 0.0000 | 0.8750 | 0.0000 |  |
| P6 | 7.3750 | 9.0000 | 0.0000 | 0.0000 | 0.8750 |  |
| P7 | 7.3750 | 9.1250 | 0.0000 |  |  |  |
| P8 | 9.3018 | 9.1250 | 0.0000 |  |  |  |

*  Circular interpolation coordinates are incremental from initial cutter position.

#### NC Program Listing

N010	G90	F6.0	S4584	M03				Absolute positioning mode, start up

N020	G00	X3.8750	Y3.6982	Z0.0000				Go rapid to P1

N030	G01	X3.8750	Y9.1250	Z0.0000				Go linear to P2

N040	G01	X5.6250	Y9.1250	Z0.0000				Go linear to P3

N050	G01	X5.6250	Y9.0000	Z0.0000				Go linear to P4

N060	G03	X6.5000	Y8.1250	Z0.0000	I0.8750	J0.0000		Go CCW to P5 – qtr. circle interp.

N070	G03	X7.3750	Y9.0000	Z0.0000	I0.0000	J0.8750		Go CCW to P6 – qtr. circle interp.

N080	G01	X7.3750	Y9.1250	Z0.0000				Go linear to P7

N090	G01	X9.3018	Y9.1250	Z0.0000				Go linear to P8

N100	G01	X3.8750	Y3.6982	Z0.0000				Go linear to P1

N110	G00	X2.0000	Y2.0000	Z8.0000	M05	M02	M30	Go rapid to P0, stop spindle, rewind

# Text boxes

2.5”

5”

5”

1”