Lab 08:  PLC Programming Lab

I.  Purpose

- Provide an introduction to the Siemens PLC ladder logic programming system

- Provide experience with the programming and debugging of ladder logic systems

- Design a functional PLC-controlled, single-cycle, automatic drilling machine

II. Practice

Your team is assigned the task of designing a system to control a single-cycle, automatic drilling machine for producing two ¼ inch diameter blind holes, at a depth of ¼ inch using four pneumatic actuators, the bench top drill press, four inductive sensors and the Siemens PLC .  You are to document the process in your engineering notebooks.

The following Inputs and Outputs are provided on each of the workbenches:

Using the Symbol Table definitions and the initial network rungs provided in the file: IENG 475 Project Start, test, create, and debug/verify the operation of the system.  Provide the Logic Expressions and Ladder Logic Rungs (Networks) for each of the following outputs:

CLAMP =

IFP2 =

FDDN =

H1D =

H2D =

Create one, team, lab report, and turn in your report to your team box by the due date.