Lab 05X:  Saving a MasterCAM IGES File in SolidWorks

Follow the procedure below to generate the SD Mines moniker on your project designs:

- Select the File>Save As from the pull down menu.

- Select the Save As Type pull down button from the window, and select IGES.

- Select the Options… button.  Check the check buttons for only the following:

  - IGES Solids/Surfaces

  - IGES Wireframe (3D Curves)

  - Export 3D Curve Features

  - Export Sketch Entities

  - Use high trim accuracy

- Select the Surface Representation pull down button and select MASTERCAM.

- Select OK.

- Save your part file to your floppy drive, and give it a name similar to T#LIDxxx, where the # is your team number, and the xxx are your initials.