## Slide 1: Primary Machining Parameters
Cutting Speed – (v)
  Primary motion
  Peripheral speed m/s ft/min
Feed – (f)
  Secondary motion
  Turning: mm/rev in/rev
  Milling: mm/tooth in/tooth
Depth of Cut – (d)
  Penetration of tool below original work surface
  Single parameter mm in
Resulting in Material Removal Rate – (MRR)
MRR* = v f d mm3/s in3/min
  where v = cutting speed; f = feed; d = depth of cut
  * general model, only!

## Slide 2: Machining Operations & Parameters
Operation Type | Speed | Feed | Depth of Cut
Turning: workpiece rotates single point cutting | Surface speed (periphery) of workpiece | Parallel to the workpiece axis* (except parting/grooving) | Tool penetration below original work surface
Drilling: tool rotates single pass cutting | Surface speed (periphery) of tool | Parallel to the tool axis | Tool penetration below original work surface (depth of hole)
Milling: tool rotates multi-point cutting | Surface speed (periphery) of tool | Perpendicular to the tool axis | Tool penetration below original work surface

## Slide 3: Cut Types: Roughing & Finishing
Cut Type | Number of Passes | Speed | Feed | Depth of Cut
Roughing: removes large amounts to get close to shape | 1 + | Low | High 0.4 - 1.25 mm/ .015 - .050 in/ | High 2.5 - 20 mm .100 - .750 in
Finishing: achieves final dimensions, tolerances, and finish | 1 - 2 | High | Low 0.125 - 0.4 mm/ .005 - .015 in/ | Low 0.75 - 2.0 mm .030 - .075 in

## Slide 4: Machining Calculations: Turning
Spindle Speed - N (rpm)
    v = cutting speed
    Do = outer diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per rev
Depth of Cut – d (mm -or- in)
    Do = outer diameter
    Df = final diameter
Machining Time - Tm (min)
    L = length of cut
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)*
*This equation is the SDSM&T form!
k = 1000 mm/m for metric units
-or-
k = 12 in/ft for U.S. customary units

## Slide 5: Machining Calculations: Turning
Spindle Speed - N (rpm)
    v = cutting speed
    Do = outer diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per rev
Depth of Cut - d (mm -or- in)
    Do = outer diameter
    Df = final diameter
Machining Time - Tm (min)
    L = length of cut
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)*
* This approximate equation assumes that f has units of mm or inches – in accordance with Groover and Rufe (SME) texts.
CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION!

## Slide 6: Machining Calculations: Turning
Spindle Speed - N (rpm)
    v = cutting speed
    Do = outer diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per rev
Depth of Cut - d (mm -or- in)
    Do = outer diameter
    Df = final diameter
Machining Time - Tm (min)
    L = length of cut
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)*
* This approximate equation assumes that d is small compared to D0 – in accordance with DeGarmo, et. al. texts.
CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION!

## Slide 7: Machining Calculations: Turning
Spindle Speed - N (rpm)
    v = cutting speed
    Do = outer diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per rev
Depth of Cut - d (mm -or- in)
    Do = outer diameter
    Df = final diameter
Machining Time - Tm (min)
    L = length of cut
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)*
In this equation: – in accordance with Kalpakjian, et. al. texts.
CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION! CAUTION!

## Slide 8: Machining Calculations: Drilling
Spindle Speed - N (rpm)
    v = cutting speed
    D = tool diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per rev
Machining Time - Tm (min)
  Through Hole :
    t = thickness
     = tip angle
  Blind Hole :
    d = depth
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)
Alternatively:

## Slide 9: Machining Calculations: Milling
Spindle Speed - N (rpm)
    v = cutting speed
    D = cutter diameter
Feed Rate - fr (mm/min -or- in/min)
    f = feed per tooth
    nt = number of teeth
Machining Time - Tm (min)
  Slab Milling:
    L = length of cut
    d = depth of cut
  Face Milling:
    w = width of cut
    2nd form is multi-pass
Mat’l Removal Rate - MRR (mm3/min -or- in3/min)
-or-
r
w d f
MRR
=

## Slide 10: Power and Energy Relationships
Power requirements to perform machining can be computed from:
Pc = Fc v N-m/s (W) ft-lb/min
where: Pc = cutting power;
Fc = cutting force; and
v = cutting speed
Customary U.S. units for power are Horsepower
(= 33000 ft-lb/min)

## Slide 11: Power and Energy Relationships
The Gross machine power (Pg) available is:
Pc = Pg• E
where E = mechanical efficiency of machine tool
Typical E for machine tools =  80 - 90%
  Note: Alternate relationships for the same -

## Slide 12: Unit Power in Machining
Useful to convert power into power per unit volume rate of metal cut
Called the unit power, Pu or unit horsepower, HPu
or
where MRR = material removal rate

## Slide 13: Specific Energy in Machining
Unit power (Pu) is also known as the specific energy (U), or the power required to cut a unit volume of material:
where t0 = un-deformed chip thickness;
w = width of the chip; and
Fc = cutting force
Units for specific energy are typically N‑m/mm3 (same as J/mm3) or as in‑lb/in3
Table on Materials page approximates specific energy for several materials based on estimated hardness